SAMPLE SPECIFICATION: L-823 Airfield Lighting Primary Connector Kits

for Unshielded (Unscreened) Cable

Electrical connections between primary cable and isolating transformers, and for splicing primary cable, shall be by means of FAA L-823 type primary connector kits properly sized to the cable being used. These kits shall conform to all of the following requirements: Each kit shall consist of a Style 3 (plug) and Style 10 (receptacle), and shall meet all requirements of FAA AC 150/5345-26 (latest revision) (Type I, Class B), verified by inclusion in the current version of FAA AC 5345-53 (latest revision) Appendix 3.